## Slide 1
Resolve
115K Quad
389 Quad
As data from Fugro’s Resolve system is also available in the area, information from this system will be examined. Here, is shown contoured data from the Resolve system with the Resolve flightlines. Underlain in the coloured contour is the aeromag data from the AeroTem survey. Flight lines for AeroTem are the thin white lines in the colour contours

## Slide 2
Co-axial inphase – 3282Hz
The main magnetic features in the cut-out has its high roughly at L7090 in the AeroTem survey. However, the main feature strikes E-W and intersects the closest Resolve Line – 14490. 2 anomalies are identified on Line 14490 at 6991240N and 6991375N

## Slide 3
Shown below are CDI sections from the Resolve data using an adapted Sengpiel Depth technique.

## Slide 4
Model 1
Line 14513 is more less a uniform response as indicated by CDI section which indicates a fairly flat
layered structure at least to some depth. Below, a 1D model is extracted from the CDI. We are generally
looking for a representative host description both to investigate the AeroTem responses and also to build
a 3D model in which to study the AeroTem responses.

## Slide 5
Model 1
Model 2
By iterative modelling, the best background model was adapted from model 1 to model 2.

## Slide 6
115K
25K
6K
data
Model1
Model2
CDI
Here is shown the quadrature data, estimated data under the CDI and Model1 and Model2. It should be remembered that the CDI technique determines resistivities for each frequency independently from other frequencies.

## Slide 7
6080
1574
389
data
Model1
Model2
CDI

## Slide 8
Quadrature spectral response for a swath of data stations/

## Slide 9
data
Model1
Model2
CDI
Spectral comparisons from a representative point in the swath.

## Slide 10
Occam Inversion
Inversion of quadrature only. Note, less resistive cover than from CDI.

## Slide 11
data
Model1
Model2
CDI
Inversion

## Slide 12
Inphase
data
Model1
Model2
CDI
Comparison of Inphase spectral response.
Note: CDI uses inphase to invert for equivalent height.
Note: High frequency In-phase for best models too high when compared to data. However, a model which gives such a low 115K inphase, is not consistent with either the high frequency quad or the 25K inphase

## Slide 13
Quad
Inphase
Model 2
best
data
The overall best model, note a tradeoff is made
between the 2 high frequency inphase responses.

## Slide 14
Quadrature
Inphase
Comparison of “best” model and Model 2 to the co-axial data.
Note: Model_482 is what is termed Model 2 for this report.

## Slide 15
Magnetic Structure
Having examined the background response of the Resolve, we now turn to the
aeromagnetic data and here we will utilize the aeromag data from the AeroTem survey.

## Slide 16
Magnetic Structure
6m
30m
62m
125m
584362East
k=.018
k=.007
Initially, 3D Euler depths were run to determine the
depths and general locations of the magnetic sources.
With this information, we then performed a
3D inversion.
Images of the resulting inverson grid are shown here.
To the left, the most magnetic features are shown
and in the bottom a cutout is made at 584362E.
Susceptibilities are in SI units.

## Slide 17
Magnetic Structure
6991304 North
584427 East
Depth = 40m
L7090
units
SI x 10-4
3D interpolated inverse magnetic grid.
Cut-outs.

## Slide 18
Magnetic Structure
looking South
L7090
k=.018
k=.015
k=.01
data
model
4 Prism model
From the inversion grid, a block model was
generated and tweaked to a good fit.
The structures are striking E-W, dipping
to the north and plunging to the west.
2 shallow structures are identified, a strong
deeper structures and North extension on L7080.

## Slide 19
3D EM Model for Resolve
389Hz Inphase
The 389Hz Inphase is contoured to the left and the
3D magnetics model inlaid in a surface representation
of the 389Hz inphase response.

## Slide 20
3D EM Model for Resolve
- Line 14490
Model directly from
AeroQuest Magnetics
x
x


Initial modelling indicated that deep structure
and northern structure had little effect (X’s)/
The (2) structures marked with a checks remained for the
3D Resolve modelling.


The 3D magnetics model from the aeromag was
imported to the Resolve survey and we show to the
left the 3D model with L14490 positioned over it.
adjusted initial model
Notes: 

## Slide 21
3D EM Model for Resolve
- Line 14490
Based on the previous background model and the Occam inversion shown here, the initial background model was 4000 Ohm-m over a very resistive magnetic basement. The initial 3D model was the 2 shallow structures from the magnetic model. Small modifications in this initial
model led to a close fit to the low frequency inphase data. A resistivity of 50 ohm-m was assign
to the (2) 3D prisms and they were given the susceptibility as in the magnetic model.
Occam Inversion
Notes: 

## Slide 22
3D EM Model for Resolve
- Line 14490
Coplanar Inphase 389Hz
CoAxial Inphase 3282Hz
Coplanar Inphase 1574Hz
Model response from the 2 remaining shallow magnetic bodies. A weak resistivity contrast is given against the host.
data
model
data
model
Notes: 

## Slide 23
3D EM Model for Resolve
- Line 14490
Coplanar Inphase 115KHz
Coplanar Quadrature 115KHz
The basic shallow magnetic features have a simple current channelling and magnetostatic response. Sensistivity to susceptibility is good but not to resistivity. We call the model – “Deep Features” but this term refers to the Resolve deep features not the aeromag. As can be seen from these figures, (2) shallow structures are missing from the model.
Notes: 

## Slide 24
3D EM Model for Resolve
The Resolve data is consistent up to this stage with the magnetic data. No indications to this stage of IP effects are seen in the Resolve data. If, in any way, the cover material is not very resistive then the 2 high frequency modeled responses are too high compared with the data. If the general IP model of the AeroTem data is used for a cover till then the response is significantly to high down to at least 1000Hz. Even for small tau, at high frequency (100KHz), the impedance has a significant imaginary component and this causes a significant effect at the 2 highest frequencies. Only if the chargeability (m) of the till is kept extremely small and the resistivity, very high, cover will the high frequency quadrature response be anywhere close to the data.
Two things are to be considered, however, at this time. The first is the extremely low response of the 115KHz inphase data as discussed before but also evident in this line. Second are the two high spatial frequency anomalies which are obviously shallower than the main features from the magnetics.
No conclusion for the first issue has been found but a
satisfactory 3D modelling of 2 shallow structures has
been done. These (2) structures are weakly conducting
with a weak inductive response added to their galvanic
response. No indication of an IP response has been found
in the IP data.
deep
shallow

## Slide 25
3D EM Model for Resolve – June 15th Model
data
deep features
deep + shallow

## Slide 26
115K Quad
115K Inphase
400Hz Quad
25K Inphase
25KHz Inphase is by far the worst fit of all 12 data
However, the objective was not to find a perfect fit
3D EM Model for Resolve – June 15th Model

## Slide 27
L7080 AeroTEM
L14490 Resolve
aeromag underlay
L7080 AeroTEM
deep structures
from Resolve model
N
shallow

## Slide 28
AeroTem modelling of Resolve and Aeromagnetic Structures

## Slide 29
Comparison of Ch1 (Off) Aerotem with the 115K Quadrature.

## Slide 30
Comparison of Ch9 (Off) Aerotem with the 389Hz Inphase.
389Hz Inphase

## Slide 31
AeroTem – 5 early off-time channels
1 2 3 4 5
1
2
3
4
5
The first 5 off-time channels are displayed over the Resolve model. The responses are shown each
channel to their own scale. It is fairly evident the response in Ch1 is simply decaying and oscillating
into the first 5 channels. After that the shape is similar but begins to break up in nose.

## Slide 32
AeroTem Modelling of Resolve Structures - Deep
last on-time Channel. The modelled response is high as it includes the magnetostatic response
of the deeper targets. My understanding of the AeroTem system is that the magnetostatic
cannot be differentiated from the freeair during on-time and thus it is removed in the bucking
process.
data
model

## Slide 33
AeroTem Modelling of Resolve Structures - Deep
1st off-time Channel. The modelled response is very low as the conductivity is
too low for such a high response. A higher conductivity for these targets is inconsistent with
the Resolve data. Although, there could be small local features of higher conductivity as this
line is slightly east of the resolve line. However, the basic response is that of (2) relatively
long wavelength targets.
data
model

## Slide 34
AeroTem Modelling of Resolve Structures - Deep
1st off-time Channel for data and last on-time data for model!
This could be supportive of a leakage of the on-time response into the off-time and a then
ensuing decay and oscillation when combined with page 52 and all the other information.
data
model