## Slide 1
Setting Moving FDEM systems in EMIGMA
Normally, the Horizontal coordinate system is used for such systems in EMIGMA.
X
Y
X
Y
Horizontal Coordinate System
direction of unit vectors change with profile direction
X̂ and Ŷ are horizontal and Ẑ is up.
X̂ is directed parallel to the tangent of the profile at each station.
Ŷ is perpendicular to the tangent at each station
the station locations are your normal GPS or grid values
The coordinate system
Transmitters and Receivers
System Components
the transmitter and receiver are both wound coils
a current is injected into the transmitter coil and this produces a magnetic moment.
the magnetic field caused by the transmitter and the ground running through the receiver coil produces a voltage which is output
the voltage output can be converted to a value of magnetic field coupling with the coil if desired
the measured magnetic field is aligned with the moment of the receiver coil
mathematically the source and receiver are defined as point electric dipoles – this is satisfactory as the coils are small with respect to the tx-rx separations
transmitter
M̂
receiver
Ĥ
A
V

## Slide 2
Setting Moving FDEM systems in EMIGMA
Data Processing
Normalization
Instrument Aspects
a square wave current of a certain frequency is injected into the transmitter
the fundamental harmonic of this boxcar is extracted in the receiver which produces a real part and an imaginary part
the real part is inphase with the current in the transmitter
the imaginary part is out of phase with the current
tx
rx
current in the transmitter
output voltage (ω) or (f)
Re
Imag
Inphase – a common name for the real part of the output
Quadrature – a common name for the imaginary part of the output
primary field
ground response
Normalization
the strongest field is that directly from the transmitter which contains no part of the ground response
this direct (primary) field is inphase and can be computed if the coil strength and the current are known
this primary field is removed from the output voltage either by computation or by the use of a bucking coil (e.g. airborne systems)
the remaining voltage is the ground response
the remaining or secondary voltage is then divided by the primary voltage which was previously subtracted
the resulting voltage output is then dimensionless
depending upon the manufacturer the resulting voltage can be adjusted to different units
complex plane

## Slide 3
Setting Moving FDEM systems in EMIGMA
Data Processing
Normalization 2
Normalization
there are two types of systems – rigid and flexible
in a rigid system, the tx and rx are housed in a rigid structure so that the separation of tx and rx is fixed – e.g. EM38, EM31, GEM2
in a flexible system, the tx and rx are independent and connected via a cable of some sort – e.g. Promis, MaxMin, EM34
in a flexible system care must be taken to ensure the cable is at the prescribed length and the coils are coplanar
tx
rx
separation
tx
rx
separation
rigid
system
flexible system
system
Additional Comments
in an airborne system, the tx and rx and housed in a bird which is flexible during flight and thus normally a bucking coil is used to reduce and normalize to the primary response
in the PROMIS system, 3 components of the secondary field are measured simultaneously and so the coil orientation of tx and rx should be made accurately
in the older MaxMin system, one can measure Hx as well as Hz but the orientation of the receiver coils in both cases must be made accurately

## Slide 4
Setting Moving FDEM systems in EMIGMA
Data Units
Data Units
the raw response is always calculated according to the formula below
this ratio, however, can be expressed in various units as below
Response (Re, Im) = { Measured Voltage (Re,Im) – Primary Field }
____________________________________
Primary Field
InPhase Units – Percent (%), PPT, PPM
Quadrature Units – Percent (%), PPT, PPM, apparent conductivity
Data Units Apparent Conductivity
it should be noted that the word "apparent" is extremely important for understanding these units
this does mean actual conductivity, but rather the ratio expressed in terms of an approximate formula which represents an equivalent halfspace for the ground and not the actual ground conductivity
the formula assumes a halfspace for the ground and then only one (1) term in the accurate representation from physical principles of such a system

## Slide 5
Setting Moving FDEM systems in EMIGMA
Data Units – apparent conductivity
Data Units Apparent Conductivity
it should be noted that the word "apparent" is extremely important for understanding these units
this does mean actual conductivity, but rather the ration expressed in terms of an approximate formula which represents an equivalent halfspace for the ground and not the actual ground conductivity
the formula assumes a halfspace for the ground and then only one (1) term in accurate representation of such a system from physical principles
in the formula below "s" is the distance between transmitter and receiver. This formula assumes no effect from the (1/s) term in the response
if indeed the ground is a halfspace then the expression is most accurate when the induction number,
[ σ ωυ0 s2 ] is small
σapp = 4 ( H )quadrature
ωυ0 s2 Hprimary

## Slide 6
Setting Moving FDEM systems in EMIGMA
Tx-Rx separations in EMIGMA
X
Y
Horizontal Coordinate System
direction of unit vectors change with profile direction
X̂ and Ŷ are horizontal and Ẑ is up.
X̂ is directed parallel to the tangent of the profile at each station.
Ŷ is perpendicular to the tangent at each station
the station locations are your normal GPS or grid values
these conventions are for the source and receiver dipoles as well as the TX-RX separations
separations may be defined as any ( dx,dy,dz) with respect to the profile direction
( dx, 0, 0 )
( 0, dy, 0 )
profile direction
inline separation
crossline separation

## Slide 7
Setting Moving FDEM systems in EMIGMA
Tx-Rx separations in EMIGMA
Some Examples
standard horizontal coplanar inline system configuration (HCP):
Tx – Mz ; Rx – Hz ; separation ( dx, 0, 0 )
[ EM38 – (1,0,0) , EM31 – (3.66,0,0)
standard horizontal coplanar crossline system configuration (HCP):
Tx – Mz ; Rx – Hz ; separation ( 0, dy, 0 )
standard vertical coplanar in line system configuration (VCP):
Tx – My ; Rx – Hy ; separation ( dx, 0, 0 )
standard vertical coplanar crossline system configuration (broadside VCP):
Tx – Mx ; Rx – Hx ; separation ( 0, dy, 0 )

## Slide 8
Setting Moving FDEM systems in EMIGMA
Configuration Page Example in EMIGMA – EM38
System Configurations
1: standard HCP
2: standard VCP
3: standard HCP crossline
4: standard VCP crossline, broadside
1. Mz, Hz, (1,0,0)
2. My, Hy, (1,0,0)
3. Mz, Hz, (0,1,0)
4. Mx, Hx, (0,1,0)

## Slide 9: Opening a database
Select a Database
Or
Create a New Database
Note: If Creating a new database,
it is recommended to put the
new database in a new subdirectory

## Slide 10: Importing Data - 1
Import a dataset
Usually, Yes
1
2
3
Select
Select EM31

## Slide 11: Importing Data - 2
1
Select System
2
Browse
for
XYZ
columnar
datafile
For other systems select Unknown
and give it a name

## Slide 12: Importing Data - 3
If your file does not contain a Header line with our specific
annotation then use ‘Set Header line’ to set the header.
Use the provided example file for assistance.

## Slide 13: Importing Data - 3b
Note 1: Dipole orientations may be X,Y, or Z. These are in reference to the ‘Horizontal”
co-ordinate system (Manual). For example, Z-Z is horizontal co-planar and Y-Y or X-X or vertical coplanar. Y is perpendicular to line and X is tangential to the line.
Note 2: Separations may be dX, dY or dZ. dX is along line while dY is across line.
For example, a dipole configuration with X-X and a separation of (0,dy,0) is vertical co-planar ‘broadside’.

## Slide 14: Importing Data - 4
Check that the import
has recognized the columns correctly.
Set the height of the
instrument.
Check the data units.
Note:
mS/m is not an actual data unit. The data has been converted by the instrument manufacturer through an approximation to this unit. EMIGMA converts it back to the original data units. You may later display in these approximate units.

## Slide 15: Importing Data - 5
You may choose not to import all profiles or decimate the data.
In addition, if you require
sub-metre accuracy in your data positioning you may
wish to strip off the leading numbers of the UTM positions

## Slide 16: Importing Data - 6
If using an EM31-R, then
your data is probably positioned at a common Tx reference point. This is because the data is collected from a common Tx antennae
Note: The centre point of the 3 Rx-Tx data are not the same.
Run Import:

## Slide 17: Importing Data - Final
You will find a new project and then use Survey Editor to see the survey positions
for multiple lines

## Slide 18: Calculating Apparent Resistivity
Calculate the best fitting half-space app rho
choose which data elements to use
e.g. for EM34 then Quadrature is default
Calculate the best fitting half-space app rho
for any dipole-dipole frequency EM data
airborne or ground
Store to new dataset or attach to original data

## Slide 19: Plotting Data - 1
( V90_tutorial .pdf for more details)
app rho display
converts normalized
data to app rho
through short separation
algebraic formula
For apparent conductivity:
Settings -> Custom -> App Cond

## Slide 20: Plotting Data - 2
app rho display
use calculated best fit
apparent resistivity
for apparent conductivity
Settings -> Custom -> App Cond

## Slide 21: Gridding data - 1
Interpolate to Grid
interpolate to regular grid
Select Components
Set Grid Settings

## Slide 22: Gridding data - 2
Interpolate to Grid
View Grids
View Grid Characteristics

## Slide 23: Viewing Gridded Data - 1
Grid Presentation
Contour

## Slide 24: Viewing Gridded Data - 2
Contour

## Slide 25: 1D FEM Inversion - 1
data points for selected profile
Invert single profile or All profiles
Optimized conjugate-gradient
or Occam, Linear Regression
and Marquardt

## Slide 26: 1D FEM Inversion - 2
contents of *.mod file
point by point information
Single line depth contour
available only for single line inversions
automatic save to database
Save to database after completion

## Slide 27: 1D FEM Inversion - 3
The *.pex file is a columnar ASCII file
inside your database directory
Use CDI Viewer for viewing models
inversion results saved to database
contains synthetic data under the model
with the model attached – (*.pex)

## Slide 28: 1D FEM Inversion - 4
Legend
CDI Viewer
Apply Contour
Select Line
ModelUnits
2D Interpolation
Colour Distribution
Equal Range – intervals equal
Equal Weight – distribution equal
Horizontal Axis selection
Plot of Resistivity vs. Depth for single point

## Slide 29: 1D FEM Inversion - 5
3D Volume Contour
(with Inversion model dataset selected)
Axis Scaling Model Units Section Cutting